## Slide 1: CS161 – Design and Architecture of Computer Systems
ISA

## Slide 2: ISA vs. Microarchitecture
ISA
  Agreed upon interface between software and hardware
    SW/compiler assumes, HW promises
  What the software writer needs to know to write and debug system/user programs
Microarchitecture
  Specific implementation of an ISA
  Not visible to the software
Microprocessor
  ISA, uarch, circuits
  “Architecture” = ISA + microarchitecture
Microarchitecture
ISA
Program
Algorithm
Problem
Circuits
Electrons
Notes: ISA is the interface between hardware and software… It is a contract that the hardware promises to satisfy.
Builder/user interface

## Slide 3: ISA vs. Microarchitecture
What is part of ISA vs. Uarch?
  Gas pedal?
    interface for “acceleration”
  Internals of the engine?
    implement “acceleration”
Implementation (uarch) can be various as long as it satisfies the specification (ISA)
  x86 ISA has many implementations: 286, 386, 486, Pentium, Pentium Pro, Pentium 4, Core, …
Which one changes faster? Microarchitecture or ISA?
  Few ISAs (x86, ARM, SPARC, MIPS, Alpha) but many uarchs
  Why?

## Slide 4: ISA
Instructions
  Opcodes, Addressing Modes, Data Types
  Instruction Types and Formats
  Registers, Condition Codes
Memory
  Address space, Addressability, Alignment
  Virtual memory management
Call, Interrupt/Exception Handling
Access Control, Priority/Privilege
I/O: memory-mapped vs. instr.
Power and Thermal Management
And many more…

## Slide 5: Microarchitecture
Implementation of the ISA under specific design constraints and goals
Anything done in hardware without exposure to software
  Pipelining
  In-order versus out-of-order instruction execution
  Memory access scheduling policy
  Speculative execution
  Superscalar processing (multiple instruction issue?)
  Caching? Levels, size, associativity, replacement policy
  Prefetching?

## Slide 6: Property of ISA vs. Uarch?
ADD instruction’s opcode
Number of general purpose registers
Number of ports to the register file
Number of cycles to execute the MUL instruction
Whether or not the machine employs pipelined instruction execution
Remember
  Microarchitecture: Implementation of the ISA under specific design constraints and goals

## Slide 7: Tradeoffs: Soul of Computer Architecture
ISA-level tradeoffs
Microarchitecture-level tradeoffs
Computer architecture is the science and art of making the appropriate trade-offs to meet a design point

## Slide 8: ISA-level tradeoffs

## Slide 9: Many Different ISAs Over Decades
x86
IBM 360
CDC 6600
SIMD ISAs
VLIW ISAs
RISC ISAs: Alpha, MIPS, SPARC, ARM
MIPS as the example throughout the course
What are the fundamental differences?
  E.g., how instructions are specified and what they do
  E.g., how complex are the instructions

## Slide 10: ISA-level Tradeoffs: Semantic Gap
Where to place the ISA? Semantic gap
  Closer to high-level language (HLL)  Small semantic gap, complex instructions
  Closer to hardware control signals?  Large semantic gap, simple instructions
RISC vs. CISC machines
  RISC: Reduced instruction set computer
  CISC: Complex instruction set computer

## Slide 11: ISA-level Tradeoffs: Semantic Gap
Some tradeoffs (for you to think about):
Simple compiler, complex hardware vs. complex compiler, simple hardware
Burden of backward compatibility
Performance? Energy Consumption?
  Optimization opportunity: who (compiler vs. hardware) puts more effort into optimization?
  Instruction size, code size

## Slide 12: Complex vs. Simple Instructions
Complex instruction: An instruction does a lot of work, e.g. many operations
  Insert in a doubly linked list
  Compute FFT
  String copy
Simple instruction: An instruction does small amount of work, it is a primitive using which complex operations can be built
  Add
  XOR
  Multiply

## Slide 13: Complex vs. Simple Instructions
Advantages of Complex instructions
  + smaller code size  better memory utilization
  + Simpler compiler: no need to optimize small instructions as much
Disadvantages of Complex Instructions
  - More complex hardware  translation from a high level to control signals and optimization needs to be done by hardware

## Slide 14: A Note on RISC vs. CISC
Usually, …
RISC
  Simple instructions
  Fixed length
  Uniform decode
  Few addressing modes
CISC
  Complex instructions
  Variable length
  Non-uniform decode
  Many addressing modes

## Slide 15: A Note on ISA Evolution
ISAs have evolved to reflect/satisfy the concerns of the day
Examples:
  Limited on-chip and off-chip memory size
  Limited compiler optimization technology

## Slide 16: MIPS ISA

## Slide 17: MIPS ISA
Different than the other mips 
  Microprocessor without Interlocked Pipelined Stages
Used as the example throughout the course
Stanford MIPS commercialized by MIPS Technologies (www.mips.com)
Large share of embedded core market
  Applications in consumer electronics, network/storage equipment, cameras, printers, …
Typical of many modern ISAs
  See MIPS Reference Data tear-out card

## Slide 18: MIPS ISA
Design principles
  small, regular & simple design  fast
  make the common case fast
Features
  32 32-bit registers, r0 = 0 always
  only load and store instructions access memory
  32-bit instructions, fixed size opcode, leftmost 6 bits
    fixed-field decoding
  all ALU operations are 3 address register operations
    add r1, r2, r3, meaning: r1  r2 + r3

## Slide 19: MIPS Instruction Format
R-type, 3 register operands
I-type, 2 register operands and 16-bit immediate operand
J-type, 26-bit immediate operand
Simple Decoding
  4 bytes per instruction, regardless of format
  must be 4-byte aligned (2 lsb of PC must be 2b’00)
  format and fields easy to extract in hardware
R-type
0
6-bit
rs
5-bit
rt
5-bit
rd
5-bit
shamt
5-bit
funct
6-bit
opcode
6-bit
rs
5-bit
rt
5-bit
immediate
16-bit
I-type
opcode
6-bit
immediate
26-bit
J-type
Notes: Quickly.

## Slide 20: MIPS R-format Instructions
Instruction fields
  op: operation code (opcode)
  rs: first source register number
  rt: second source register number
  rd: destination register number
  shamt: shift amount (00000 for now)
  funct: function code (extends opcode)
Used only for ALU instructions
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits

## Slide 21: R-format Example
add $r8, $r17, $r18
special
$r17
$r18
$r8
0
add
0
17
18
8
0
32
000000
10001
10010
01000
00000
100000
000000100011001001000000001000002 = 0232402016
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits

## Slide 22: Arithmetic Operations
Add and subtract, three operands
  Two sources and one destination
add a, b, c # a gets b + c
All arithmetic operations have this form
Design Principle 1: Simplicity favours regularity
  Regularity makes implementation simpler
  Simplicity enables higher performance at lower cost

## Slide 23: Arithmetic Example
C code:
f = (g + h) - (i + j);
Compiled MIPS code:
add t0, g, h # temp t0 = g + h add t1, i, j # temp t1 = i + j sub f, t0, t1 # f = t0 - t1

## Slide 24: Register Operands
Arithmetic instructions use register operands
MIPS has a 32 × 32-bit register file
  Use for frequently accessed data
  Numbered 0 to 31
  32-bit data called a “word”
Assembler names
  $t0, $t1, …, $t9 for temporary values
  $s0, $s1, …, $s7 for saved variables
Design Principle 2: Smaller is faster
  c.f. main memory: millions of locations
  Accessing register file is much faster than memory

## Slide 25: The Constant Zero
MIPS register 0 ($zero) is the constant 0
  Cannot be overwritten
Useful for common operations
  E.g., move between registers
  add $t2, $s1, $zero

## Slide 26: Register Operand Example
C code:
f = (g + h) - (i + j);
  f, …, j in $s0, …, $s4
Compiled MIPS code:
add $t0, $s1, $s2 add $t1, $s3, $s4 sub $s0, $t0, $t1

## Slide 27: MIPS I-format Instructions
Immediate arithmetic and load/store instructions
  rt: destination or source register number
  Constant: –215 to +(215 – 1), used as immediate
  Address: offset added to base address in rs
Good design demands good compromises
  Different formats complicate decoding, but allow 32-bit instructions uniformly
  Keep formats as similar as possible
op
rs
rt
immediate or offset
6 bits
5 bits
5 bits
16 bits

## Slide 28: I-format Example: load
lw $r8, 8($r17), $r8  Mem[8+$r17]
lw
$r17
$r8
3510
17
8
8
100011
10001
01000
0000000000001000
100011100010100000000000000010002 = 8E28000816
op
rs
rt
immediate or offset
6 bits
5 bits
5 bits
16 bits
constant or address

## Slide 29: I-format Example: store
sw $r8, 8($r17), Mem[8+$r17]  $r8
sw
$r17
$r8
4310
17
8
8
101011
10001
01000
0000000000001000
101011100010100000000000000010002 = AE28000816
op
rs
rt
immediate or offset
6 bits
5 bits
5 bits
16 bits
constant or address

## Slide 30: I-format Example: addi
addi $r8,$r17, 8 $r8  8+$r17
addi
$r17
$r8
810
17
8
8
001000
10001
01000
0000000000001000
001000100010100000000000000010002 = 2228000816
op
rs
rt
immediate or offset
6 bits
5 bits
5 bits
16 bits
constant or address

## Slide 31: I-format Example: beq
beq $r8,$r17, 8 if ($r8==$r17) PC  PC+4+8
beq
$r17
$r8
410
17
8
8
000100
10001
01000
0000000000001000
000100100010100000000000000010002 = 1228000816
op
rs
rt
offset
6 bits
5 bits
5 bits
16 bits
offset

## Slide 32: Memory vs. Registers
MIPS is a Load/Store Register File machine
  Instructions compute only on data in the Register File
  Example:
    add R3, R2, R1
    All data needs to be in the Register File
  But we only have 32 registers in the Register File
Most data is stored in Memory (large, but slow)
Need to transfer the data to the Register File to use it
  Load: load data from memory to the Register File (lw instruction)
  Store: store data to the memory from Register File(sw instruction)
Hence, MIPS is a Load/Store Register File machine

## Slide 33: Memory Organization in MIPS
Register File (small and fast)
32 bits
Compute
(Add, Sub, Multiply, etc.)
R0
R1
R2
.
.
.
R31
Memory
(big and slow)
8 bits
Read/Write
Data
Load data
Store data

## Slide 34: Memory and Register File
R31
32 Registers
4 Billion Memory Locations
32 bits
8 bits
0
Memory
Register File
0
1
2
…
4,294,967,295
(=232 -1)
R0
R1
R2
…
How many memory locations do we need to fill a register in the Register File?
1 word
1 word

## Slide 35: Memory Operands
Main memory used for composite data
  Arrays, structures, dynamic data
To apply arithmetic operations
  Load values from memory into registers
  Store result from register to memory
Memory is byte addressable
  Each address identifies an 8-bit byte
Words are aligned in memory
  Address must be a multiple of 4

## Slide 36: Memory Operand Example 1
8?
32?
C code:
g = h + A[8];
  g in $s1, h in $s2, base address of A in $s3
Compiled MIPS code:
lw $t0, ($s3) # load word
add $s1, $s2, $t0
offset
base register
  Index 8 requires offset of 32
  (4 bytes per word)

## Slide 37: Memory Operand Example 2
C code:
A[12] = h + A[8];
  h in $s2, base address of A in $s3
Compiled MIPS code:
  Index 8 requires offset of 32
lw $t0, 32($s3) # load word add $t0, $s2, $t0 sw $t0, 48($s3) # store word

## Slide 38: Immediate Operands
Constant data specified in an instruction
addi $s3, $s3, 4
No subtract immediate instruction
  Just use a negative constant
  addi $s2, $s1, -1
Design Principle 3: Make the common case fast
  Small constants are common
  Immediate operand avoids a load instruction

## Slide 39: 32-bit Constants
0000 0000 0011 1101 0000 0000 0000 0000
Most constants are small
  16-bit immediate is sufficient
For the occasional 32-bit constant
lhi rt, constant
  Copies 16-bit constant to left 16 bits of rt
  Clears right 16 bits of rt to 0
lhi $s0, 61
0000 0000 0111 1101 0000 1001 0000 0000
ori $s0, $s0, 2304

## Slide 40: Byte/Halfword Operations
Could use bitwise operations
MIPS byte/halfword load/store
  String processing is a common case
lb rt, offset(rs) lh rt, offset(rs)
  Sign extend to 32 bits in rt
lbu rt, offset(rs) lhu rt, offset(rs)
  Zero extend to 32 bits in rt
sb rt, offset(rs) sh rt, offset(rs)
  Store just rightmost byte/halfword

## Slide 41: Conditional Operations
Branch to a labeled instruction if a condition is true
  Otherwise, continue sequentially
beq rs, rt, L1
  if (rs == rt) branch to instruction labeled L1;
bne rs, rt, L1
  if (rs != rt) branch to instruction labeled L1;
j L1
  unconditional jump to instruction labeled L1

## Slide 42: Announcements
Assignment 1 will be posted today and is due Monday 29th April in class.
We will have a makeup class during next week
  This class will get recorded for people that can’t make it

## Slide 43: Compiling If Statements
C code:
if (i==j) f = g+h; else f = g-h;
  f, g, … in $s0, $s1, …
Compiled MIPS code:
bne $s3, $s4, Else add $s0, $s1, $s2 j Exit Else: sub $s0, $s1, $s2 Exit: …

## Slide 44: Compiling Loop Statements
C code:
  while (save[i] == k) i += 1;
  i in $s3, k in $s5, address of save in $s6
Compiled MIPS code:
Loop: sll $t1, $s3, 2 add $t1, $t1, $s6 lw $t0, 0($t1) bne $t0, $s5, Exit addi $s3, $s3, 1 j Loop Exit: …

## Slide 45: More Conditional Operations
Set result to 1 if a condition is true
  Otherwise, set to 0
slt rd, rs, rt
  if (rs < rt) rd = 1; else rd = 0;
slti rt, rs, constant
  if (rs < constant) rt = 1; else rt = 0;
Use in combination with beq, bne
  slt $t0, $s1, $s2 # if ($s1 < $s2) bne $t0, $zero, L # branch to L

## Slide 46: Signed vs. Unsigned
Signed comparison: slt, slti
Unsigned comparison: sltu, sltui
Example
  $s0 = 1111 1111 1111 1111 1111 1111 1111 1111
  $s1 = 0000 0000 0000 0000 0000 0000 0000 0001
  slt $t0, $s0, $s1 # signed
    –1 < +1  $t0 = 1
  sltu $t0, $s0, $s1 # unsigned
    +4,294,967,295 > +1  $t0 = 0

## Slide 47: Branch Instruction Design
Why not blt, bge, etc?
Hardware for <, ≥, … slower than =, ≠
  How to do it? Combine slt with beq
beq and bne are the common case
This is a good design compromise

## Slide 48: Branch Addressing
Branch instructions specify
  Opcode, two registers, target address
Most branch targets are near branch
  Forward or backward
op
rs
rt
constant or address
6 bits
5 bits
5 bits
16 bits
PC-relative addressing
  Target address = PC + offset × 4
  PC already incremented by 4 by this time

## Slide 49: Jump Addressing
Jump (j and jal) targets could be anywhere in text segment
  Encode full address in instruction
op
address
6 bits
26 bits
(Pseudo)Direct jump addressing
  Target address = PC31…28 : (address × 4)

## Slide 50: MIPS ISA Register Names

## Slide 51: MIPS Instruction Formats

## Slide 52: Addressing Mode Summary

## Slide 53: Synchronization
Two processors sharing an area of memory
  P1 writes, then P2 reads
  Data race if P1 and P2 don’t synchronize
    Result depends of order of accesses
Hardware support required
  Atomic read/write memory operation
  No other access to the location allowed between the read and write
Could be a single instruction
  E.g., atomic swap of register ↔ memory
  Or an atomic pair of instructions

## Slide 54: Synchronization in MIPS
Load linked: ll rt, offset(rs)
Store conditional: sc rt, offset(rs)
  Succeeds if location not changed since the ll
    Returns 1 in rt
  Fails if location is changed
    Returns 0 in rt
Example: atomic swap (to test/set lock variable)
  try: add $t0,$zero,$s4 ;copy exchange value
  ll $t1,0($s1) ;load linked
  sc $t0,0($s1) ;store conditional
  beq $t0,$zero,try ;branch store fails
  add $s4,$zero,$t1 ;put load value in $s4

## Slide 55: review slides
this was covered in CS 61 or CS 120A

## Slide 56: Unsigned Binary Integers
Given an n-bit number
Range: 0 to +2n – 1
Example
  0000 0000 0000 0000 0000 0000 0000 10112 = 0 + … + 1×23 + 0×22 +1×21 +1×20 = 0 + … + 8 + 0 + 2 + 1 = 1110
Using 32 bits
  0 to +4,294,967,295

## Slide 57: 2s-Complement Signed Integers
Given an n-bit number
Range: –2n – 1 to +2n – 1 – 1
Example
  1111 1111 1111 1111 1111 1111 1111 11002 = –1×231 + 1×230 + … + 1×22 +0×21 +0×20 = –2,147,483,648 + 2,147,483,644 = –410
Using 32 bits
  –2,147,483,648 to +2,147,483,647

## Slide 58: 2s-Complement Signed Integers
Bit 31 is sign bit
  1 for negative numbers
  0 for non-negative numbers
–(–2n – 1) can’t be represented
Non-negative numbers have the same unsigned and 2s-complement representation
Some specific numbers
  0: 0000 0000 … 0000
  –1: 1111 1111 … 1111
  Most-negative: 1000 0000 … 0000
  Most-positive: 0111 1111 … 1111

## Slide 59: Signed Negation
Complement and add 1
  Complement means 1 → 0, 0 → 1
Example: negate +2
  +2 = 0000 0000 … 00102
  –2 = 1111 1111 … 11012 + 1 = 1111 1111 … 11102

## Slide 60: Sign Extension
Representing a number using more bits
  Preserve the numeric value
In MIPS instruction set
  addi: extend immediate value
  lb, lh: extend loaded byte/halfword
  beq, bne: extend the displacement
Replicate the sign bit to the left
  c.f. unsigned values: extend with 0s
Examples: 8-bit to 16-bit
  +2: 0000 0010 => 0000 0000 0000 0010
  –2: 1111 1110 => 1111 1111 1111 1110

## Slide 61: Hexadecimal
Base 16
  Compact representation of bit strings
  4 bits per hex digit
0 | 0000 | 4 | 0100 | 8 | 1000 | c | 1100
1 | 0001 | 5 | 0101 | 9 | 1001 | d | 1101
2 | 0010 | 6 | 0110 | a | 1010 | e | 1110
3 | 0011 | 7 | 0111 | b | 1011 | f | 1111
Example: eca8 6420
  1110 1100 1010 1000 0110 0100 0010 0000

## Slide 62: Logical Operations
Instructions for bitwise manipulation
Operation | C | Java | MIPS
Shift left | << | << | sll
Shift right | >> | >>> | srl
Bitwise AND | & | & | and, andi
Bitwise OR | ¦ | ¦ | or, ori
Bitwise NOT | ~ | ~ | nor
Useful for extracting and inserting groups of bits in a word

## Slide 63: Shift Operations
shamt: how many positions to shift
Shift left logical
  Shift left and fill with 0 bits
  sll by i bits multiplies by 2i
Shift right logical
  Shift right and fill with 0 bits
  srl by i bits divides by 2i (unsigned only)
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits

## Slide 64: AND Operations
Useful to mask bits in a word
  Select some bits, clear others to 0
and $t0, $t1, $t2
0000 0000 0000 0000 0000 1101 1100 0000
0000 0000 0000 0000 0011 1100 0000 0000
$t2
$t1
0000 0000 0000 0000 0000 1100 0000 0000
$t0

## Slide 65: OR Operations
Useful to include bits in a word
  Set some bits to 1, leave others unchanged
or $t0, $t1, $t2
0000 0000 0000 0000 0000 1101 1100 0000
0000 0000 0000 0000 0011 1100 0000 0000
$t2
$t1
0000 0000 0000 0000 0011 1101 1100 0000
$t0

## Slide 66: NOT Operations
Useful to invert bits in a word
  Change 0 to 1, and 1 to 0
MIPS has NOR 3-operand instruction
  a NOR b == NOT ( a OR b )
nor $t0, $t1, $zero
0000 0000 0000 0000 0011 1100 0000 0000
$t1
1111 1111 1111 1111 1100 0011 1111 1111
$t0
Register 0: always read as zero