## Slide 1: CS161 – Design and Architecture of Computer Systems
Caches, Caches, Caches $$$$$

## Slide 2: Memory (Programmer’s View)

## Slide 3: Performance Gap
The memory wall

## Slide 4: Memory Systems
How can we supply the CPU with enough data to keep it busy?
We will focus on memory issues,
  which are frequently bottlenecks that limit the performance of a system.
Ideal memory: large, fast and cheap
Memory
Processor
Input/Output
Storage | Speed | Cost | Capacity | Delay | Cost/GB
Static RAM | Fastest | Expensive | Smallest | 0.5 – 2.5 ns | $1,000’s
Dynamic RAM | Slow | Cheap | Large | 50 – 70 ns | $10’s
Hard disks | Slowest | Cheapest | Largest | 5 – 20 ms | $0.1’s

## Slide 5: The Problem
Ideal memory’s requirements oppose each other
Bigger is slower
  Bigger  Takes longer to determine the location
Faster is more expensive
  Memory technology: SRAM vs. DRAM vs. Disk vs. Tape
Higher bandwidth is more expensive
  Need more banks, more ports, higher frequency, or faster technology

## Slide 6: Why Memory Hierarchy?
We want both fast and large
But we cannot achieve both with a single level of memory
Idea: Have multiple levels of storage (progressively bigger and slower as the levels are farther from the processor) and ensure most of the data the processor needs is kept in the fast(er) level(s)

## Slide 7: How to make such memory hierarchy?
fast
small
big but slow
move what you use here
backup
everything
here
With good locality of reference, memory appears as fast as
and as large as
faster per byte
cheaper per byte

## Slide 8: Memory in a Modern System
CORE 1
L2 CACHE 0
SHARED L3 CACHE
DRAM INTERFACE
CORE 0
CORE 2
CORE 3
L2 CACHE 1
L2 CACHE 2
L2 CACHE 3
DRAM BANKS
DRAM MEMORY CONTROLLER

## Slide 9: Typical Memory Hierarchy
Principle of locality:
A program accesses a relatively small portion of the address space at a time
Two different types of locality:
  Temporal locality: if an item is referenced, it will tend to be referenced again soon
  Spatial locality: if an item is referenced, items whose addresses are close tend to be referenced soon

## Slide 10: How to Create the Illusion of Big and Fast
Memory hierarchy – put small and fast memories closer to CPU, large and slow memories further away

## Slide 11: Introducing caches
Introducing a cache – a small amount of fast, expensive memory.
  The cache goes between the processor and the slower, dynamic main memory.
  It keeps a copy of the most frequently used data from the main memory.
Memory access speed increases overall, because we’ve made the common case faster.
  Reads and writes to the most frequently used addresses will be serviced by the cache.
  We only need to access the slower main memory for less frequently used data.
Lots of
dynamic RAM
A little static
RAM (cache)
CPU

## Slide 12: The principle of locality
One’s recent past is a very good predictor of his/her near future.
Temporal Locality: If you just did something, it is very likely that you will do the same thing again soon
  since you are here today, there is a good chance you will be here again and again regularly
Spatial Locality: If you did something, it is very likely you will do something similar/related (in space)
  every time I find you in this room, you are probably sitting close to the same people

## Slide 13: Memory locality
Why does the hierarchy work?
Because most programs exhibit locality, which the cache can take advantage of.
  The principle of temporal locality says that if a program accesses one memory address, there is a good chance that it will access the same address again.
  The principle of spatial locality says that if a program accesses one memory address, there is a good chance that it will also access other nearby addresses.

## Slide 14: How caches take advantage of locality
First time the processor reads from an address in main memory, a copy of that data is also stored in the cache.
  The next time that same address is read, we can use the copy of the data in the cache instead of accessing the slower dynamic memory.
  So the first read is a little slower than before since it goes through both main memory and the cache, but subsequent reads are much faster.
This takes advantage of temporal locality—commonly accessed data is stored in the faster cache memory.
By storing a block (multiple words) we also take advantage of spatial locality
Lots of
dynamic RAM
A little static
RAM (cache)
CPU

## Slide 15: Temporal locality in instructions
Loops are excellent examples of temporal locality in programs.
  The loop body will be executed many times.
  The computer will need to access those same few locations of the instruction memory repeatedly.
For example:
  Each instruction will be fetched over and over again, once on every loop iteration.
Loop: lw $t0, 0($s1)
add $t0, $t0, $s2
sw $t0, 0($s1)
addi $s1, $s1, -4
bne $s1, $0, Loop

## Slide 16: Temporal locality in data
Programs often access the same variables over and over, especially within loops. Below, sum and i are repeatedly read and written.
Commonly-accessed variables can sometimes be kept in registers, but this is not always possible.
  There are a limited number of registers.
  There are situations where the data must be kept in memory, as is the case with shared or dynamically-allocated memory.
sum = 0;
for (i = 0; i < MAX; i++)
sum = sum + f(i);

## Slide 17: Spatial locality in instructions
Nearly every program exhibits spatial locality, because instructions are usually executed in sequence — if we execute an instruction at memory location i, then we will probably also execute the next instruction, at memory location i+1.
Code fragments such as loops exhibit both temporal and spatial locality.
sub $sp, $sp, 16
sw $ra, 0($sp)
sw $s0, 4($sp)
sw $a0, 8($sp)
sw $a1, 12($sp)

## Slide 18: Spatial locality in data
Programs often access data that is stored contiguously.
  Arrays, like a in the code on the top, are stored in memory contiguously.
  The individual fields of a record or object like employee are also kept contiguously in memory.
employee.name = “Homer Simpson”;
employee.boss = “Mr. Burns”;
employee.age = 45;
sum = 0;
for (i = 0; i < MAX; i++)
sum = sum + a[i];

## Slide 19: Cache basics

## Slide 20: Cache
Generically, any structure that “memoizes” frequently used results to avoid repeating the long-latency operations required to reproduce the results from scratch.
Most commonly in the on-die context: an automatically-managed memory hierarchy based on SRAM
  memoize in SRAM the most frequently accessed DRAM memory locations to avoid repeatedly paying for the DRAM access latency

## Slide 21: Caching basics
Block (line): Unit of storage in the cache
  Memory is logically divided into cache blocks that map to locations in the cache
A cache hit
  occurs if the cache contains the data that we’re looking for. Hits are good, because the cache can return the data much faster than main memory.
A cache miss
  occurs if the cache does not contain the requested data. This is bad, since the CPU must then wait for the slower main memory.
There are two basic measurements of cache performance.
  The hit rate is the percentage of memory accesses that are handled by the cache.
  The miss rate (1 - hit rate) is the percentage of accesses that must be handled by the slower main RAM.
  Typical caches have a hit rate of 95% or higher, so in fact most memory accesses will be handled by the cache and will be dramatically faster.

## Slide 22: Four important questions
1. When we copy a block of data from main memory to the cache, where exactly should we put it?
2. How can we tell if a word is already in the cache, or if it has to be fetched from main memory first?
3. Eventually, the small cache memory might fill up. To load a new block from main RAM, we’d have to replace one of the existing blocks in the cache... which one?
4. How can write operations be handled by the memory system?
Questions 1 and 2 are related—we have to know where the data is placed if we ever hope to find it again later!

## Slide 23: Direct-Mapped Cache: Placement and Access
Assume byte-addressable memory: 256 bytes, 8-byte blocks  32 blocks
Assume cache: 64 bytes, 8 blocks
  Direct-mapped: A block can go to only one location
  Addresses with same index contend for the same location
    Cause conflict misses
Tag store
Data store
Address
tag
index
byte in block
3 bits
3 bits
2b
V
tag
=?
MUX
byte in block
Hit?
Data

## Slide 24: Direct-Mapped Caches
Direct-mapped cache: Two blocks in memory that map to the same index in the cache cannot be present in the cache at the same time
  One index  one entry
Can lead to 0% hit rate if more than one block accessed in an interleaved manner map to the same index
  Assume addresses A and B have the same index bits but different tag bits
  A, B, A, B, A, B, A, B, …  conflict in the cache index
  All accesses are conflict misses

## Slide 25: Set Associativity
Addresses 0 and 8 always conflict in direct mapped cache
Instead of having one column of 8, have 2 columns of 4 blocks
Tag store
Data store
V
tag
=?
V
tag
=?
Address
tag
index
byte in block
3 bits
2 bits
3b
Logic
MUX
MUX
byte in block
Key idea: Associative memory within the set
+ Accommodates conflicts better (fewer conflict misses)
-- More complex, slower access, larger tag store
SET
Hit?

## Slide 26: Higher Associativity
4-way
+ Likelihood of conflict misses even lower
-- More tag comparators and wider data mux; larger tags
Tag store
Data store
=?
=?
=?
=?
MUX
MUX
byte in block
Logic
Hit?

## Slide 27: Full Associativity
Fully associative cache
  A block can be placed in any cache location
Tag store
Data store
=?
=?
=?
=?
=?
=?
=?
=?
MUX
MUX
byte in block
Logic
Hit?

## Slide 28: One more detail: the valid bit
When started, the cache is empty and does not contain valid data.
We should account for this by adding a valid bit for each cache block.
  When the system is initialized, all the valid bits are set to 0.
  When data is loaded into a particular cache block, the corresponding valid bit is set to 1.
So the cache contains more than just copies of the data in memory; it also has bits to help us find data within the cache and verify its validity.
00
01
10
11
Index
Tag
Data
00
11
01
01
00 + 00 = 0000
Invalid
???
???
Main memory
address in cache block
1
0
0
1
Valid
Bit

## Slide 29: Memory Hierarchy Basics
When a word is not found in the cache, a miss occurs:
  Fetch word from lower level in hierarchy, requiring a higher latency reference
  Lower level may be another cache or the main memory
  Also fetch the other words contained within the block
    Takes advantage of spatial locality
  Place block into cache in any location within its set, determined by address

## Slide 30: Sets and ways for direct-mapped, set associative, and fully associative cache
block/line |  |  | 
Sets: Block mapped by addr
Ways: Block can go anywhere
n-way set associative (in this example, it’s a 4-way set associative cache)
Example: Assume that your cache has 16 blocks.

## Slide 31: Direct-mapped Cache
block/line
16 Sets
1-way
Direct mapped cache
Each block maps to only one cache line
aka
1-way set associative

## Slide 32: Set Associative Cache
block/line |  |  | 
4 Sets
4-way
n-way set associative
Each block can be mapped to a set of n-lines Set number is based on block address (4-way set associative)

## Slide 33: Fully Associative Cache
block /line |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1 Sets
16-ways
Fully associative
Each block can be mapped to any cache line
aka
m-way set associative where m = size of cache in blocks

## Slide 34: Cache Addressing
block/line |  |  | 
s-Sets: Block mapped by addr
n-Ways: Block can go anywhere
m = size of cache in blocks
n = number of ways b = block size in bytes
Tag (remainder) bits = 32-s-b | Index (sets) bits = log2s | Offset (block size) bits = log2b
Address
Cache size = s * n * b
# of Sets (s) = m / n

## Slide 35: Cache Addressing
Ex. 64KB cache, direct mapped, 16 byte block
m = size of cache in blocks
n = number of ways b = block size in bytes
Tag (remainder) bits = 32-s-b | Index (sets) bits = log2s | Offset (block size) bits = log2b
Address
Cache size = s * n * b
# of Sets (s) = m / n
16 | 12 | 4
Notes: 4k sets = 2^12

## Slide 36: Cache Addressing
Ex. 64KB cache, 2-way assoc., 16 byte block
m = size of cache in blocks
n = number of ways b = block size in bytes
Tag (remainder) bits = 32-s-b | Index (sets) bits = log2s | Offset (block size) bits = log2b
Address
Cache size = s * n * b
# of Sets (s) = m / n
17 | 11 | 4
Notes: 2k sets = 2^11

## Slide 37: Cache Addressing
Ex. 64KB cache, fully assoc., 16 byte block
m = size of cache in blocks
n = number of ways b = block size in bytes
Tag (remainder) bits = 32-s-b | Index (sets) bits = log2s | Offset (block size) bits = log2b
Address
Cache size = s * n * b
# of Sets (s) = m / n
28 | 0 | 4
Notes: 1 set = 2^0

## Slide 38: What if the cache fills up?
Our third question was what to do if we run out of space in our cache, or if we need to reuse a block for a different memory address.
A miss causes a new block to be loaded into the cache, automatically overwriting any previously stored data.

## Slide 39: Eviction/Replacement Policy
Which block in the set to replace on a cache miss?
  Any invalid block first
  If all are valid, consult the replacement policy
    Random
    FIFO
    Least recently used
    Least frequently used?
    Hybrid replacement policies
    Optimal replacement policy?

## Slide 40: Replacement Policy (cont’d)
Direct mapped: no choice
Set associative
  Prefer non-valid entry, if there is one
  Otherwise, choose among entries in the set
Least-recently used (LRU)
  Choose the one unused for the longest time
    Simple for 2-way, manageable for 4-way, too hard beyond that
Random
  Gives approximately the same performance as LRU for high associativity

## Slide 41: Cache Replacement Policies--Example
Picks which block to replace within the set
Example: LRU (00 means Most Recently Used, and 11 is Least Recently Used)
Line 0 | 01
Line 1 | 00
Line 2 | 11
Line 3 | 10
Line 0 | 10
Line 1 | 01
Line 2 | 11
Line 3 | 00
Hit on Line 3
Line 0 | 10
Line 1 | 01
Line 2 | 00
Line 3 | 11
Miss

## Slide 42: Handling Writes
  When do we write the modified data in a cache to the next level?
    Write through: At the time the write happens
    Write back: When the block is evicted
  Write-back
    + Can consolidate multiple writes to the same block before eviction
      Potentially saves bandwidth between cache levels + saves energy
  -- Need a bit in the tag store indicating the block is “dirty/modified”
  Write-through
    + Simpler
    + All levels are up to date. Consistency: Simpler cache coherence because no need to check lower-level caches
    -- More bandwidth intensive; no coalescing of writes

## Slide 43: Write-Through
On data-write hit, could just update the block in cache
  But then cache and memory would be inconsistent
Write through: also update memory
But makes writes take longer
  e.g., if base CPI = 1, 10% of instructions are stores, write to memory takes 100 cycles
    Effective CPI = 1 + 0.1×100 = 11
Solution: write buffer
  Holds data waiting to be written to memory
  CPU continues immediately
    Only stalls on write if write buffer is already full

## Slide 44: Write-Back
Alternative: On data-write hit, just update the block in cache
  Keep track of whether each block is dirty
When a dirty block is replaced
  Write it back to memory
  Can use a write buffer to allow replacing block to be read first

## Slide 45: What to do in a write miss?
Do we allocate a cache block on a write miss?
  Allocate on write miss: Yes
  No-allocate on write miss: No
Allocate on write miss
  + Simpler because write misses can be treated the same way as read misses
No-allocate
  + Conserves cache space if locality of writes is low (potentially better cache hit rate)

## Slide 46: Measuring Cache Performance
Components of CPU time
  Program execution cycles: Includes cache hit time
  Memory stall cycles: Mainly from cache misses
With simplifying assumptions:
Example:
  Given:
    I-cache miss rate = 2%, D-cache miss rate = 4%, Miss penalty = 100 cycles, Base CPI (ideal cache) = 2, Load & stores are 36% of instructions
  Miss cycles per instruction
    I-cache: 0.02 × 100 = 2
    D-cache: 0.36 × 0.04 × 100 = 1.44
  Actual CPI = 2 + 2 + 1.44 = 5.44
    Ideal CPU is 5.44/2 =2.72 times faster

## Slide 47: Average Access Time
Hit time is also important for performance
Average memory access time (AMAT)
  AMAT = Hit time + Miss rate × Miss penalty
Example
  CPU with 1ns clock, hit time = 1 cycle, miss penalty = 20 cycles, I-cache miss rate = 5%
  AMAT = 1 + 0.05 × 20 = 2ns
    2 cycles per instruction

## Slide 48: Classification of Cache Misses
Compulsory miss
  first reference to an address (block) always results in a miss
  subsequent references should hit unless the cache block is displaced for the reasons below
Capacity miss
  cache is too small to hold everything needed
  defined as the misses that would occur even in a fully-associative cache (with optimal replacement) of the same capacity
Conflict miss
  defined as any miss that is neither a compulsory nor a capacity miss

## Slide 49: How to Reduce Each Miss Type
Compulsory
  Caching cannot help
  Prefetching
    Prefetching is the act of predicting future memory accesses and fetching those that are not already in the cache before the processor explicitly asks for them
Conflict
  More associativity
Capacity
  Utilize cache space better: keep blocks that will be referenced

## Slide 50: Multilevel Caches
Primary cache attached to CPU
  Small, but fast
Level-2 cache services misses from primary cache
  Larger, slower, but still faster than main memory
Main memory services L-2 cache misses
Some high-end systems include L-3 cache

## Slide 51: Multilevel Cache Example
Given
  CPU base CPI = 1, clock rate = 4GHz
  Miss rate/instruction = 2%
  Main memory access time = 100ns
With just primary cache
  Miss penalty = 100ns/0.25ns = 400 cycles
  Effective CPI = (0.98 ×1) + (0.02 ×(1+400)) = 9
Now add L-2 cache
  Access time = 5ns
  L-2 miss rate = 25%
  CPI = (0.98 ×1) + 0.02 ×((0.75 ×21) + (0.25 ×421)) = 3.4
  Performance ratio = 9/3.4 = 2.6

## Slide 52: Multilevel Cache Considerations
Primary cache
  Focus on minimal hit time
L2 cache
  Focus on low miss rate to avoid main memory access
  Hit time has less overall impact