## Slide 1: Error Correcting Codes
CS 161

## Slide 2: why error correcting codes
noise in communication channels causes errors
  e.g. WiFi, Bluetooth, etc.
  sent: 0011 0010 1101
  received: 0010 0110 1101
wires in circuits can act like antennas
  electromagnetic radiation becomes digital data
single event upset (SEU)
  cosmic particles collide with atoms in atmosphere, create showers of ionized particles (neutrons, protons), these can discharge transistors.
  the smaller the transistor geometry, the lower the energy needed to keep its state

## Slide 3: the Hamming SEC code
Hamming distance
  Number of bits that are different between two binary strings
  Hd (a, b) = population count (a XOR b)
General case (non binary): edit distance
  Given two strings of equal length, it is the minimum number of substitutions required to change one strings into another:
    sent OHLALA!
    received OHLALU!
    edit distance = 1

## Slide 4: parity
to binary strings of size n (word),
  add one extra bit (parity bit) such that the number of 1’s is always even (even parity)
⇒ the Hamming distance between any two correct words is 2
⇒ if a word has an odd number of 1s, one of its bits is in error
we cannot tell which one though
Minimum distance = 2
  provides single bit error detection (parity code)
Minimum distance = 3
  provides single error correction, 2 bit error detection

## Slide 5: parity bit - SED
Parity bit
  is an additional bit set to make the number of 1s even (or odd) in that word
  it is a Single Error Detection (SED) mechanism.
  in case of an error, the data is re-transmitted or re-fetched from memory.
7-bit data | #1s | 8-bits with parity | 
 |  | even | odd
0000000 | 0 | 00000000 | 00000001
0001111 | 4 | 00011110 | 00011111
0000111 | 3 | 00001111 | 00001110
1111111 | 7 | 11111111 | 11111110

## Slide 6: parity checking
b0
b1
b2
b3
b5
b6
b7
p
∑
generating a parity bit
checking the parity
check bit
error if check bit != 0
two or an even number of errors are not detected
b4
b0
b1
b2
b3
b5
b6
b7
p
∑
b4

## Slide 7: Hamming code [7,4]
Simplest Hamming code:
  4 bits of data (d1:d4) and 3 parity bits (p1:p3)
  [7,4] means total 7 bits, data is 4 bits
  each parity bit covers 3 data bits
  the Hamming distance of every encoded word is now 3
  so it is possible to detect and correct a single error
  but the decoder cannot distinguish between a single-bit error of a code word and the double-bit error of another code word

## Slide 8: Hamming code [8,4]
Add a parity bit to the whole code word of the [7,4]
  increases the Hamming distance to 4
  allows SEC/DED
    (i.e single error correction or double error detection)

## Slide 9: encoding SECDED
Hamming code [12,8]
  can achieve Single Error Correction (SEC) and Double Error Detection (DED)
To calculate Hamming code:
  Number bits from 1 on the left
  All bit positions that are a power 2 are parity bits
  Each parity bit covers certain data bits:
    Bit 1 (0001) for bits (1, 3, 5, 7, 9, 11, …): XXX1
    Bit 2 (0010) for bits (2, 3, 6, 7, 10, 11, 14, 15, …): XX1X
    Bit 4 (0100) for bits (4-7, 12-15, 20-23, …): X1XX
    Bit 8 (1000) for bits (8-15, 24-31, 40-47, …): 1XXX
    Note that each bit is covered by two or more parity bits.
  Set parity bits to create even parity for each group.

## Slide 10: SECDED table [12,8]
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
 | p1 | p2 | d1 | p4 | d2 | d3 | d4 | p8 | d5 | d6 | d7 | d8
data |  |  |  |  |  |  |  |  |  |  |  | 
p1 |  |  |  |  |  |  |  |  |  |  |  | 
p2 |  |  |  |  |  |  |  |  |  |  |  | 
p4 |  |  |  |  |  |  |  |  |  |  |  | 
p8 |  |  |  |  |  |  |  |  |  |  |  | 
encoded data |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 11: decoding SEC (12,8)
Value of parity bits indicates which bits are in error
  Use numbering from encoding procedure
  Textbook example: value = 10011010 (8 bits)
  Encoded value = 011100101010 (12 bits: 8 data + 4 parity)
    Parity bits = 0110 indicates no error
Assume bit 3 is flipped: 010100101010
  Compute the new parity bits:
    P1 - (bits 1,3,5,7,9,11: 0,0,0,1,1,1), Should be 1. ERROR
    P2 - (bits 2,3,6,7,10,11: 1,0,0,1,0,1). Should be 0. ERROR
    P4 - (bits 4-7, 12: 1,0,0,1,0). CORRECT
    P8 - (bits 8-12: 0,1,0,1,0). CORRECT
  Parity bits 1 and 2 are in error, 1+2 = 3 ← the bit in error

## Slide 12: example
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
 | p1 | p2 | d1 | p4 | d2 | d3 | d4 | p8 | d5 | d6 | d7 | d8
data |  |  | 1 |  | 0 | 0 | 1 |  | 1 | 0 | 1 | 0
p1 | 0 |  | 1 |  | 0 |  | 1 |  | 1 |  | 1 | 
p2 |  | 1 | 1 |  |  | 0 | 1 |  |  | 0 | 1 | 
p4 |  |  |  | 1 | 0 | 0 | 1 |  |  |  |  | 0
p8 |  |  |  |  |  |  |  | 0 | 1 | 0 | 1 | 0
encoded data | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0

## Slide 13: example (2)
Assume bit 3 is flipped
  bits 1 and 2 are incorrect
  1+2 = 3, the bit position in error
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
 | p1 | p2 | d1 | p4 | d2 | d3 | d4 | p8 | d5 | d6 | d7 | d8
encoded data | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0
p1 | 0 |  | 0 |  | 0 |  | 1 |  | 1 |  | 1 | 
p2 |  | 1 | 0 |  |  | 0 | 1 |  |  | 0 | 1 | 
p4 |  |  |  | 1 | 0 | 0 | 1 |  |  |  |  | 0
p8 |  |  |  |  |  |  |  | 0 | 1 | 0 | 1 | 0

## Slide 14: SEC/DEC code
Add an additional parity bit for the whole word (pn)
Make Hamming distance = 4
Decoding:
  Let H = SEC parity bits
    H even, pn even, no error
    H odd, pn odd, correctable single bit error
    H even, pn odd, error in pn bit
    H odd, pn even, double error occurred
Note:
  ECC DRAM uses SEC/DEC with 8 bits protecting each 64 bits, they are 72-bits wide

## Slide 15: SEC generalization
  Let p number of parity bits, d number of data bits
  p parity bits can cover from 1 to (2p– 1) total bits
  there are (p+d) possible bit errors and 1 case of no error
  so 2p >= p+d+1
  so p bits provide SEC for (p+d) bits, one more bit adds DED, so we get SEC/DED
d = | 8 | 16 | 32 | 64
p = | 4 | 5 | 6 | 7
p | d | total bits | name
2 | 1 | 3 | Hamming(3,1)
3 | 4 | 7 | Hamming(7,4)
4 | 11 | 15 | Hamming(15,11)
5 | 26 | 31 | Hamming(31,26)
p | 2p - p - 1 | 2p - 1 | 

## Slide 16: example
Min number of parity bits to protect a 128-bit word using the SEC/DED?
  9 bits. How?